## Slide 1
uArcSim Implementation by AI
WYLin, 2026.05

## Slide 2
Motivation
uArcSim
  Design Flow
  Model Level
  Profile and GUI
Performance Tuning
AI Harness Engineering
Next Step
Agenda

## Slide 3
Motivation : MDLA7 L1Mesh AA Model
Solution
  MDLA6 Traffic Log and Log Player
  AA Model (Cannot get is optimization patterns before 6/E)
  Brand-New Test Framework : uArchSim
Motivation

## Slide 4
An IP accelerator modeling and verification platform by AI
AI Tool : Claude and Codex
Input documents (No violation of PIM policies)
  Block Diagram (Hand sketch)
  Throughout Table (md)
Human Resource
  Top Down ： 2 Week (WY)
  Bottom Up : 4 Weeks (PJ)
uArchSim

## Slide 5
uArcSim Design Flow
Host
Hand Sketch  Picture  Drawio (by AI)
Block Map
Throughput Table
Fast Mode
SystemC
Compiler
Download
ETHZ_v5/v6.tflit
TensorFlow
Slicer
TensorFlow
Python Golden
Document
Verliator
Simulator
CX Mode
SystemC
Batch
Regression
Profile
Waveform
Log
Yosys
Synthesis
Verilog
(hw/dpi)
Correlation
1. Gate Count
2. Synthesizable Checking

## Slide 6
MDLA7 System Block Diagram
Host
Command Engine
1T
Descriptor
CONV Engine
Requant
EWE Engine
POOL Engine
TNPS Engine
W 1T
W 1T
W 1T
W 1T
L1Mesh
3 MB
L1_Manager
32x16B R ACT
32x16B R WGT
8R/8W (16Bytes)
16R/8W
16R/8W
8R/8W
16R/16W
UDMA
16R/16W
4 GB DRAM
AXI_R
AXI_W
Legend
Payload lanes
1T config/control
Hand Sketch  Picture  Drawio (by AI)
4096b/cyc

## Slide 7
Module Functions and Throughput
Module
Function
Throughput / Modeling Point
CONV
Conv / FC / DWConv MAC
INT8x8: 16,384 MAC/cyc; 62.3 TOPS @1.9GHz
Requant
INT32/FP post-processing, clamp, scale/shift
16 CONV-chain lanes; Payload W 128 B/cyc
EWE
Add/Mul/Sub/activation/math/softmax pieces
64 elem/cyc; R 256 B/cyc, W 128 B/cyc
POOL
Max/Avg/Global pooling
R 256 B/cyc, W 128 B/cyc
TNPS
Transpose/Slice/Space-depth/Layout materialize
128 B/cyc read + 128 B/cyc write
UDMA
DRAM↔L1 copy, prefetch, store, ACT codec
LPDDR5 model peak ≈85.3 GB/s external
L1Mesh
3 MB banked scratchpad / routing fabric
16 banks x 16B per SRAM cycle backend
MDLA7 SystemC Performance Model | internal technical briefing
5
System Parameters
1.9 GHz core | 62.3 TOPS INT8x8 baseline
3 MB L1Mesh SRAM | LPDDR5X-10667, dual x32
64B descriptors via DRAM ring + MMIO doorbell

## Slide 8
Layer to Microblock architecture and compiler
Compiler / graph compiler
Compiler / tiler
Compiler + Command Engine ABI (Application Binary Interface)
Command Engine
Layer graph
↓
Layer fuse / graph-level fuse
↓
Tile split
↓
Tile-level fuse / L1 SRAM handoff
↓
Microblock pipeline / wavefront

## Slide 9
Microblock Pipeline Path for regression
Name | Scope or shape | ETHZ_v6 Slicing Patterns
Producer compute | CONV/DW/FC/EWE/POOL/TNPS -> L1 tile | 44
Consumer tail | producer -> EWE/POOL/TNPS/store | 52
Layout bridge | sslice/concat/d2space/transpose -> compute | 286
Fanout/live-range | one producer -> multiple consumers | 34
UDMA as engine | udma_r/udma_w preload/store participates in pipeline | 9
Streaming preload | udma_r head/tail -> compute overlap | 134
Scan ETHZ_v6 Patterns to generate Microblock Path Slice Patterns by AI for function coverage and easy debugging

## Slide 10
version | Meaning | source path | Batch | Speed
fast | analytical / functional SystemC model | systemc/ | run_systemc.py | 
cx | SystemC synth timing / microblock model | systemc/ | run_systemc.py --L1=cx --engine=cx | 
verilog | RTL Verilog path，control + datapath | rtl/verilog/ | run_verilog.py –-option dpi run_verilog.py | 
Modeling Level and Version

## Slide 11
Profile
7

## Slide 12
Performance Tuning
Tunning Approach
  Baseline profiling
  Tiling and micro-blocks
  Layer Fuse
  Engine Overlap Scheduling
  Engine Bubbles
Prompt Examples
  /goal E2E function 100%, turning performance 不能掉, 算法 要是 general rule
  Check ETHZ_V6 不是最後一層有大量的 DRAM Write 列出來 然後最佳化
  Check ETHZ_V6 Layer 可以Fuse 成 Flow 沒 Fuse起來的 列出來 然後最佳化
  Check ETHZ_V6 Flow 沒有切成 Microblock 列出來 然後最佳化
  Check ETHZ_V6 Flow 間 Engine 可以平行 沒有平行 列出來 然後最佳化
  Check ETHZ_V6 Flow 間 可以 Prefecth 沒有 Prefecth 列出來 然後最佳化
7

## Slide 13: MDLA7 uArchSim Regression Table
Clock
  Engine : 1.9GMHz
  SRAM : 1.3G
BW
  DRAM : LPDDR5
Computer Power
  MDLA6: 4 Cores
  MDLA7: 1 Cores ~~ MDLA6 2 Cores

## Slide 14
Modeling for L1Mesh
Methodology
  Top down (0.5 hours)
  Bottom up (2 Weeks)
Hierarchy
  SRAM Macro (1 Port R/W, 768x16Bytes, 12K)
  Quad SRAM Macro (4 Port R/W, 48K)
  Mesh4x4 (16*Quad SRAM Macro, 768K)
  L1Mesh (4*Mesh4x4,3M)
    Edge Injection match R/W Requests (32R+32W+16R+16W)
    2xMesh4x4 mapping to same 16*Quad SRAM Macro
7

## Slide 15
Regression Table & L1Mesh Evaluation
7

## Slide 16: L1Mesh Evaluation (v0.1 version)
L1Mesh Simulation Mode : Fast/SRAM Port Conflict/Mesh

## Slide 17
Verilog Simulator Comparison
評比項目 | Verilator | Icarus Verilog | 商用模擬器 (VCS/Questa)
效能 (Speed) | 極高 (最快) | 低 | 極高
精確度 (Accuracy) | 週期精確 | 全時序精確 | 全時序精確
License 費用 | $0 (開源) | $0 (開源) | 極高 (按 Core 計費)
主要用途 | SoC/CPU 功能驗證 | 單元測試/教學 | 全面簽核 (Sign-off)

## Slide 18
Verilog Run with Verilator
Verilator (Compiled)
將 RTL 直接編譯為優化的 C++/SystemC。它主要採用週期精確 (Cycle-accurate) 的模擬方式，犧牲了時序細節以換取極致的運算速度。
傳統模擬 (Event-driven)
如 Icarus Verilog。逐個事件處理，支援精確的 #delay 與四態邏輯 (X/Z)，但處理大型 SoC 時速度極慢，成為驗證瓶頸。
IEEE 1800-2017: 高度支援最新的 SystemVerilog 標準。
Assertions (SVA): 支援並行與即時斷言檢查。
VPI/DPI: 完善的 C/SystemVerilog 外掛介面支援。
限制： 預設為二態邏輯 (0/1)，有限度支持 X/Z 態。

## Slide 19
Harness Engineering 用AI 幾週的心得
目前 Codex > Claude Code > Gemini
DLA7 Project ： 10美元 玩 4小時 100美元 3天 200美元5天
AI 是一位很厲害的同仁 看完目前全世界的書 及 Paper
AI 很博學 會教你不會的知識 生成 讀書報告(未來新人訓練)
  我是剛新進公司的員工 想從基礎學習
  請幫我看文件及Code 有系統寫下150頁 讀書筆記
AI 不會幫你設計架構 但它會逼你把每個設計 decision 講清楚
  你也可以問一般業界怎麼做 把問答題變成選擇題
AI 會偷懶 要先想好很嚴謹的驗收條件
  找 ETHZ Pattern E2E Evaluation
  用別的 TOOL 來驗證它 (eg. Verilog Simulator + Correlation)
Top-down Design 比 Bottom-up 好溝通
  Context Window 有限 Compact之後就會忘了前面 重要事情還是一直要提醒
  Tod-down Design 真的不用看 Code
關機要寫 Handoff to Handoff.md 隔天開工先讀它
對它客氣一點 不要爆粗口 這樣容易它選不好的回應來回答你問題

## Slide 20
MDLA7 1-Core System
  L1Mesh Design
  L1Mesh CX Model Approach form Verilog
  Fine Tune Compile for Fast/CX Model
  CX/Verilog Correlation
Find gap of FE/IA/CX speed with simulator designed byAI
MDLA7 2-Cores System
MVPU 2.5 System
Next Step

## Slide 21
MDLA7 profile — bmm_softmax_bmm_2.5ms_1g_int8.tflite (fast)
Model: model/BMM/bmm_softmax_bmm_2.5ms_1g_int8.tflite
Compiled layers: 65 (PASS 63 / FAIL 2)
Graph coverage: complete — 0/65 compile rows skipped
Verification: per compiled-layer DRAM reference compare, including the final compiled layer; no separate original-TFLite final-output checker
Sim time: 5.749 ms @ 1.9 GHz (10,923,659 cycles)
Util: avg 24.4% / peak 55.4% (udma_w)
DRAM r/w: 142.58 / 276.82 MB
SRAM r/w: 672.29 / 579.44 MB
BMM-Softmax-BMM 第一版

## Slide 22
BMM-Softmax-BMM 第二版
MDLA7 profile — bmm_softmax_bmm_tiled_2.5ms_int8.tflite (fast)
Model: model/BMM/bmm_softmax_bmm_tiled_2.5ms_int8.tflite
Compiled layers: 1358 (PASS 1358 / FAIL 0)
Graph coverage: INCOMPLETE — 1/1359 compile rows skipped; simulator PASS covers compiled layers only
Verification: per compiled-layer DRAM reference compare, including the final compiled layer; no separate original-TFLite final-output checker
Sim time: 11.184 ms @ 1.9 GHz (21,249,675 cycles)
Util: avg 14.0% / peak 62.1% (ewe)
DRAM r/w: 161.30 / 0.00 MB
SRAM r/w: 185.57 / 301.56 MB