## Slide 1
MDLA7 MODELING STRATEGY
Fast model 與 RTL-style model 是兩種不同抽象層級，不是單純速度開關
01
Fast model = performance estimator
RTL-style model = micro-architecture timing model
這份簡報整理 coding style、interface、timing fidelity，以及下一步要怎麼往可 synthesizable RTL 前進。
FAST
高階公式
bytes/BW + ops/lanes
RTL-STYLE
phase timing
issue/decode/route/SRAM
NEXT
transaction FIFO
req/resp + arbitration
Current position
RTL-oriented SystemC
with functional datapath
and phase-level timing

## Slide 2
ABSTRACTION LADDER
Fast model 在高階估算；RTL-style 往硬體 pipeline 與 interface 靠近
02
1
Functional
copy / compute correctness
資料正確性為主
2
Fast analytical
aggregate latency formula
sweep 大量 model
3
RTL-style
phase + transaction timing
看 bubble / stall / overlap
NOW
4
Synthesizable RTL
valid-ready + cycle datapath
可轉 RTL / 對 Verilog
Less detail / faster
More detail / closer to RTL

## Slide 3
CODING STYLE + MODULE COVERAGE
Fast 是公式化 block call；RTL-style 用 phase/transaction table 表達硬體行為
03
Area
Fast model
RTL-style model
Interface
blocking C++ API
transaction wrapper; next FIFO req/resp
Timing
cycles = formula
issue / decode / read / compute / write / done
Data movement
aggregate bytes
DRAM / L1 / L1Mesh phase visibility
Debug view
engine busy / layer time
phase summary + Gantt + stall reason
Command Engine
descriptor dispatch
dispatch / cfg_fifo_write
UDMA
copy + BW wait
issue / DRAM / L1 / codec / done
CONV / Requant
analytical cycles
read / MAC / chain / pack / write
EWE / POOL / TNPS
op-level latency
read / compute / write phases
L1Manager / L1Mesh
pass-through + aggregate timing
L1ManagerReq/Resp + issue / mesh / SRAM
Boundary: RTL-style timing/interface is closer to hardware, but current datapath still uses functional memory copy.

## Slide 4
USE AND NEXT STEP
用 Fast 做 corpus sweep；用 RTL-style 找硬體風險；下一步才進 FIFO protocol
04
Use Fast when
• 跑大量 ETHZ / MLPerf
• 快速看 layer total
• 檢查 schedule / fusion 是否有效
Use RTL-style when
• 看 bubble / stall
• 比較 engine overlap
• 檢查 L1Manager / L1Mesh 壓力
Next
• req/resp FIFO
• arbitration policy
• valid-ready Payload beats
• then synthesize check
Recommended path
Keep both models: Fast remains the regression baseline; RTL-style becomes the architectural truth meter before writing RTL.

## Slide 5
TOWARD SYNTHESIZABLE RTL
可以轉，但不是一鍵轉；要新增可綜合 RTL path，保留現有 model 當 reference
05
Why current code is not synth-ready
• std::vector / dynamic allocation
• blocking read/write function calls
• wait(sc_time) timing annotation
• memcpy / variable-size buffers
• JSON/Gantt trace metadata
Conversion strategy
• keep fast / RTL-style as reference
• add systemc/include/mdla7/rtl/
• define fixed valid-ready interface
• convert modules to clocked FSM
• guard traces with #ifndef __SYNTHESIS__
First target mini path
UDMA_RTL
→ L1Manager_RTL
→ L1Mesh_RTL SRAM banks
→ DRAM AXI shim
Support linear copy first: DRAM→L1 and L1→DRAM, 16B payload beats.
Decision: do not mutate the fast model into RTL. Build a separate synthesizable path and verify it against fast + RTL-style outputs.