## Slide 1
MDLA7 SystemC Model and Performance Optimization
Architecture, module throughput, tuning history, regression status, and synthesis gaps
RISC-V Host
Cmd Engine
L1Mesh 3 MB
Compute Engines
LPDDR5X DRAM
→
→
→
→
Prepared from the current MDLA7_Codex repository and regression reports
Date: 2026-05-09
MDLA7 SystemC Performance Model | internal technical briefing
1

## Slide 2
1. Executive Summary
What was built and what is proven today
62.3 TOPS
INT8 baseline CONV target
3 MB
L1Mesh SRAM working buffer
51/51
ETHZ_V6 fast functional OK
11/11
Hotspot fast/conflict/mesh OK
Implemented a deployable SystemC/TLM model for MDLA7: command dispatch, L1Mesh, UDMA, CONV, Requant, EWE, POOL, and TNPS.
Added profile visibility: per-layer flow ID, engine lanes, fast/conflict/mesh timing, and interactive Gantt timeline support.
Optimization focus moved from layer-by-layer DRAM round trips to tiled microblock handoff and on-chip producer-to-consumer fusion.
Latest hotspot example: sd_decoder_quant_L152_L191 reduced from 0.456 ms to 0.373 ms by folding PAD into the following CONV.
Remaining work before synthesis is mostly RTL hardening: precise interfaces, cycle-accurate arbitration, verification collateral, and timing closure.
MDLA7 SystemC Performance Model | internal technical briefing
2

## Slide 3
2. Given Specification Snapshot
Architectural assumptions captured in spec.md
Compute Core
65,536 4x4 base cells
16 clusters; 4 FP-capable clusters
INT8x8 baseline: 16,384 MAC/cycle
1.9 GHz core clock
Memory System
3 MB L1Mesh SRAM
Dual 4x4 mesh, 16-bank backend
LPDDR5X-10667, dual-channel x32
85.3 GB/s DRAM peak
Programming Model
Descriptor ring in DRAM
MMIO doorbell from host
Wait/signal tags for dependencies
Per-layer profile and flow tracking
CONV ACT and WGT read paths bypass L1_Manager and directly enter L1Mesh.
CONV output is not a normal Payload W path; partial sums chain directly to Requant lanes.
Non-CONV engines share L1_Manager arbitration: Requant, EWE, POOL, TNPS, and UDMA.
SystemC keeps three timing modes: fast estimate, port-conflict, and mesh-conflict.
MDLA7 SystemC Performance Model | internal technical briefing
3

## Slide 4
3. Module Dataflow
How data moves through the current model
UDMA DRAM↔L1
L1_Manager Arbiter
L1Mesh 3 MB SRAM
CONV Direct R
Requant Chain/W
EWE / POOL Vector
TNPS Layout
↔
↔
direct ACT/WGT read
psum chain
↔
↔
UDMA handles external traffic and activation codec. TNPS now owns tensor layout movement so UDMA is not blocked by transpose/slice/space-depth work.
Microblock handoff keeps producer output in L1 and lets consumers start without intermediate DRAM writeback.
Flow ID groups fused layers in the profile report; layer ID equals flow only when fusion is not possible.
MDLA7 SystemC Performance Model | internal technical briefing
4

## Slide 5
4. Module Functions and Throughput
Current modeling contract
Module
Function
Throughput / Modeling Point
CONV
Conv / FC / DWConv MAC
INT8x8: 16,384 MAC/cyc; 62.3 TOPS @1.9GHz
Requant
INT32/FP post-processing, clamp, scale/shift
16 CONV-chain lanes; Payload W 128 B/cyc
EWE
Add/Mul/Sub/activation/math/softmax pieces
64 elem/cyc; R 256 B/cyc, W 128 B/cyc
POOL
Max/Avg/Global pooling
R 256 B/cyc, W 128 B/cyc
TNPS
Transpose/Slice/Space-depth/Layout materialize
128 B/cyc read + 128 B/cyc write
UDMA
DRAM↔L1 copy, prefetch, store, ACT codec
LPDDR model peak ≈85.3 GB/s external
L1Mesh
3 MB banked scratchpad / routing fabric
16 banks x 16B per SRAM cycle backend
Throughput numbers are the modeling/spec contract; synthesis must later replace abstract timing with RTL and physical constraints.
MDLA7 SystemC Performance Model | internal technical briefing
5

## Slide 6
5. SystemC and Profiling Deliverables
What exists in the repository now
Compiler / Runtime
TFLite to MDLA descriptor program
GraphMeta producer/consumer sidecar
Opcode lowering for CONV/EWE/POOL/TNPS/UDMA
Functional reference verification
SystemC Model
Command engine dispatch
L1Mesh timing modes
Engine-level busy cycles
Wait/signal tag scheduling
Profile Reports
Layer table: cycle, DRAM, SRAM, flow
Fast / conflict / mesh reports
Gantt waveform per engine
Flow ID and TNPS lane added
The model is designed for performance exploration: it exposes memory traffic, engine overlap, fusion boundaries, and regressions quickly.
The profile report is now used as the primary debug surface: if a layer is fused, it shares a flow ID with its producer/consumer chain.
Latest commit included TNPS layout engine, profile/Gantt TNPS lane, spec update, and PAD-to-CONV fusion.
MDLA7 SystemC Performance Model | internal technical briefing
6

## Slide 7
6. Performance Tuning Journey
From DRAM round trips to on-chip microblock handoff
1. Baseline profiling
Per-layer execution; large intermediate DRAM writes visible in profile.
2. Flow reporting
Added flow ID so fused chains are visible and unfused layers remain layer=flow.
3. Tiling and microblocks
Conv/FC/EWE/POOL handoff through L1; reduce intermediate DRAM R/W.
4. Overlap scheduling
Allow different engines to run concurrently when dependencies permit.
5. Layout offload
Moved transpose/slice/concat/space-depth style ops to TNPS lane.
6. PAD→CONV fold
Eliminated PAD materialization before 3x3 CONV; sd_decoder slice improved 18.1%.
MDLA7 SystemC Performance Model | internal technical briefing
7

## Slide 8
7. Case Study: sd_decoder_quant_L152_L191
L16 PAD bottleneck resolved by PAD→CONV fusion
0.456 ms
Before fast time
0.373 ms
After fast time
18.1%
Fast cycle reduction
0 MB
L16 DRAM R/W after
Original L16 was a PAD materialization: 55,978 cycles, ~1.09 MB DRAM read and write.
It could not overlap with L15 because L16 depends on L15 output.
The correct optimization is to remove the materialized PAD and fold the halo into L17 CONV.
Result: L16 becomes 0-cycle / 0-DRAM, and L17 joins the same flow as the producer chain.
Chart: Fast Profile Time (ms)
| Before | After
fast ms | 0.456 | 0.373
MDLA7 SystemC Performance Model | internal technical briefing
8

## Slide 9
8. Regression Status
Current functional and profile confidence
51/51
ETHZ_V6 fast-only OK
0
Function FAIL in ETHZ_V6 fast
11/11
Hotspot all modes OK
51 rows
Pattern regression recorded
ETHZ_V6 new-op record: fast-only 51/51 OK, Function FAIL 0, Skipped OP 0.
Hotspot regression: 11/11 OK for fast, conflict, and mesh profiles.
sd_decoder_quant_L152_L191 latest: fast 0.373 ms, conflict 0.506 ms, mesh 0.541 ms, all OK.
Regression reports are stored under batch/output and profile indexes under batch/profile_*.html.
Caution: conflict/mesh have not been uniformly rerun for every ETHZ_V6 pattern after every change; fast is the current gate for broad ETHZ_V6.
MDLA7 SystemC Performance Model | internal technical briefing
9

## Slide 10
9. Gap to Synthesizable RTL
What remains before true hardware sign-off
Microarchitecture RTL
Translate TLM engines to RTL state machines
Finalize descriptor CSR/ring interfaces
Define reset/clock/power domains
Harden TNPS and UDMA datapaths
Timing Accuracy
Cycle-accurate L1Mesh bank arbitration
Real DRAM controller behavior
Backpressure and FIFO sizing
Clock-domain and SRAM macro timing
Verification Closure
Golden model and random tests
Coverage for all op modes
RTL/SystemC co-simulation
Full fast/conflict/mesh regression gates
Highest-value next engineering gaps: true multi-source TNPS CONCAT, PAD/PACK/UNPACK/TILE true kernels, D2SPACE/add/maxpool/softmax intermediate write reduction, and L1Mesh contention calibration.
The current model is a strong architecture/performance exploration platform, not yet a synthesizable implementation.
Recommended next milestone: freeze descriptor ABI, build RTL skeleton per engine, and keep SystemC as the performance/reference oracle.
MDLA7 SystemC Performance Model | internal technical briefing
10